Introduction to Atmel AVR Microcontroller Programming

# Section 1 – Introduction and Setup
Welcome to BuildBrighton's Atmel AVR Microcontroller programming workshop!
In the first hour, we'll mostly be making sure you've all ready to go for coding, but before that, let's just discuss what you've got in front of you.
Thing 1: The BuildBrighton Colour Sharing Zombie Apocalypse Badge:

This is what we'll be programming, and most of you should be pretty familiar with what it can do – now we just need to show you how it does it.
The badge is comprised of the following components:
- An RGB LED (basically a red, green and blue LED in one package) – the white/clear thing.
- An infrared (IR) LED – this transmits infrared light instead of visible light – just like your TV remote. This is the purple-ish coloured thing.
- An infrared (IR) sensor – the black square on the left. This receives IR signals, from IR LEDs - just like your TV does.
- A battery – a 3V button cell to be precise, and a capacitor to help the battery out when it needs to.
- A switch – so we can turn it off when we're not playing, and save the battery life.
- An Atmel ATtiny45 microprocessor – the brains of the operation, and what we'll be programming via:
- The header pins – this is the 3x2 spikey thing next to the RGB LED. This lets us attach Thing 2 – our USB microprocessor programmer – to squirt new code onto the microprocessor.
Thing 2: A USB microprocessor programmer:
PHOTO NEEDED
The USB microprocessor programmer is a special USB device that allows a computer program running on your laptop to squirt new code and data onto the microprocessor on the badge itself – via the header pins.
Programmers are usually pretty expensive, but we've made these ones ourselves from a simple design on the internet (google Instructables vusbtiny for how we made it) – and so they're cheap enough for us to give you to take away to use at home.
So, now we know what we're going to be playing with – but what on earth is a microprocessor?!
A microprocessor – or MCU – is basically a small, fully functional computer. It's more like your PC as a whole than like the dual-core CPU monster that sits inside it. Contained within the tiny little package is a CPU, some memory, and some storage – like your harddrive. There are also several legs on it – which we call pins. These are the MCUs inputs and outputs – how it communicates with the rest of the world. Kind of like your eyes see, and mouth talks, the MCU talks and listens over these pins.
What we'll be doing over the next few hours is learning how we can control the devices available to us - the RGB LED, IR LED, and IR sensor – via writing little programs that we're going to upload to the MCU. Easy!
For now though, please relax whilst we go around and make sure everyone has a working environment for the rest of the workshop.
### Installation Instructions – Windows
You'll need WinAVR:
http://winavr.sourceforge.net/
Also, you'll need the TinyUSB driver:
http://www.ladyada.net/make/usbtinyisp/download.html
You'll also need to install MsysGit and TortoiseGit:
http://code.google.com/p/msysgit/
http://code.google.com/p/tortoisegit/downloads/list
We recommend using a decent text editor:
http://notepad-plus-plus.org/
### Installation Instructions – MacOS
You need to install the CrossPack AVR kit:
http://www.obdev.at/products/crosspack/index.html
And also Git:
http://code.google.com/p/git-osx-installer/
### Installation – Linux
You should just need to install the following packages:
avr-gcc
avrdude
git-core
# Section 2 – Making a Blinky LED Badge
We don't have a screen to display 'Hello World!' on, so for our first code, let's make an LED say 'Hi!' instead.
Take a look at the following code:
examples/1-1-blinky.c
Ignore what's going on at the start of the program for now – we'll explain that later. Take a look at the main() function – this is what gets executed.
What's happening here?
The language you are looking at is 'C'. A lot of people are scared of C. It's what's called a 'low level language', as it doesn't do a lot of stuff for you like higher level languages like Java, .NET, or Python. Luckily for us, we're not doing complicated things, so C is easy cheesy for our needs.
The language used for programming an Arduino is also C, so what you learn today will be useful for that too!
What we have in main() is an infinite loop – basically it's saying 'while 1 is true, do the stuff in the braces'. As 1 is always true in C, the loop never exits.
Inside our loop, we're turning on the Red LED, then delaying for 100,000 microseconds ('us'), then turning off all LEDs for another 100,000us. So basically we're flickering the LED 5 times a second!
Load the code onto your badge by doing:
 make install PROJECTNAME=examples/1-1-blinky
Blinky! :o)
Open up:
my_code.c
This is your code. We'll be tweaking and changing this over the course of the workshop.

Copy the code from the blinky example into it, and load it onto your badge with:
make install
Hopefully, you won't get any errors, and your badge should starting blinking away. If you do get errors, call one of us over and we'll help you figure out why.
Remember this command! You'll be using to load your code onto your badge all day long.
Can you tweak the code to make the LED flash red, then green, then blue?
Hint: use JUST_BLUE_ON and JUST_GREEN_ON
We've also made some other macros to make changing colours easier. What happens if you use:
TURN_RED_OFF TURN_RED_ON
TURN_GREEN_OFF TURN_GREEN_ON
TURN_BLUE_OFF TURN_BLUE_ON
Have a play with these macros in your my_code.c file, remembering to save, and run 'make install' to load it onto your badge!
What happens when have all on at once? What colours can you get out of the badge?
### Removing the delay
Now, the problem with our blinky code above, is that we are sleeping for long periods of time. This means that while we're sleeping, we can't really do a great deal else.
Take a look at:
examples/2-2-blinky_no_delay.c
This code does the same thing as our original blinky, but keeps the loop going. This means we can put more code in the gaps.
Load it into your badge with:
make install PROJECTNAME=examples/2-2-blinky_no_delay

The '%' symbol here means 'remainder of' – so:
1053 % 1000 == 53
5 % 2 == 1
430 % 10 == 0
This technique is used a lot. In our example, it means that our red LED is on for half of the time, and off for the other half.
Have a play around with this code, can you get it to display multiple colours? In a simple pattern?
Hint: use 'else if ( loop_counter % 200 ) { }'

### More Advanced Stuff:
- What are Macros?: take a look at include/badge.h
- What happens if you do delay_ten_us(1000000) – which should sleep for a second? Why doesn't it?
- What is PORTB?
- Introduction to binary
- Setting bits on PORTB

# Section 3: More LED colours, with PWM
Ok, so our LED is flickering and blinking away, in a multitude of colours (well, 7ish colours!). But that's not all it can do! After-all, there's no real difference between this RGB LED and a pixel on your snazzy monitor – and your monitor can display lots more colours than that.
The secret to all this is PWM – Pulse Width Modulation. By turning the LED colours off and on in quick succession, we trick your eye into believing that they are on all the time – just a bit dimmer or brighter depending on how much it's off versus how much it's on.
Open up the following code, and load it onto your badge:
make install PROJECTNAME=examples/3-1-very_basic_pwm
Your Red LED should appear quite dim now.
All that's different between this code and how we were playing with the RGB LED before is that we've got rid of the loop delay, and tweaked how quickly the red LED is being turned off and on. Rather than blinking it at a visible frequency, we flicker it so quickly that the eye can't see it flicker. This is called 'persistence of vision' – and it's how movies and old TV screens con you into thinking you're seeing a full picture. Your brain joins up the dots, so to speak.
Wibble the badge in front of your eyes really quickly – you should be able to break down the illusion, and see the led being both on and off.
In our code, we're only on for 5% of the time, and off for the other 95%. This is called a '5% duty cycle'.
What happens if you change the code to have a 2% duty cycle?
PWM is the secret to being able to display full colour on the RGB LED. For example, to make a nice yellow colour, you need to mix a little bit of red with a lot of green – examples/3-2-making_yellow.c shows you how.
What other colours can you get by mixing red, green, and blue?

### RGB Colour Mixing
Well, now we know how a little about PWM, lets bring in a function that's already tried and tested to make our lives easier. Load up:
examples/3-3-rgb_mixing.c
This uses our 'display_colour' function, which we use in the Zombie badge code. It's syntax is:
display_colour(tick_v, red_v, green_v, blue_v);
… where each v is a variable from 0 to 255.
tick_v is special, in it's just lets the function know how time is ticking along – and hence how to do the PWM. The other 3 variables tell it which intensities of red, green, and blue to use.
Copy this code into your my_code.c file, and have a play!
What colours can you make?
### Colour Cycling
Of course, being able to display one colour is all well and good, and we've learned how we can flip between colours without big delays previously.
But what about storing a list of colours to display? Then we can just change the list to what ever we fancy, rather than changing code over and over.
There are many ways to do this, but lets just keep things simple for now.
Open up:
examples/3-4-colour_cycling.c
This sets up some arrays of values for our red, green, and blue. A variable is then use to iterate through the values of this array, plugging them into our display_colour function every second.
Load this onto your badge and have a play. Can you work out how to make the sequence longer?
# Section 4: Reacting to IR
Time now to move onto IR sending and receiving – and how we can start getting the badge to do some reacting, rather than just bimbling its way through a loop of pre-programmed instructions?
Well, why don't we first get it to react to seeing an IR signal, and reset the pattern if it does?
To do this, we need to read from the OUT pin on our IR sensor, and if it's HIGH (1) then we know that the IR sensor is seeing a suitable signal.
Take a look at:
examples/session4-ir1/1-flash_ir.c
Flash it to your badge with:
make install PROJECTNAME=examples/4-1-flash_ir
Can you import this code into your colour cycling code, so that the cycle resets on seeing IR from a remote control?
### Sending IR signals
So our badge now can react to an IR signal being sent to it, but how does it send one itself?
To do that, we need a little bit of technical knowhow about how IR sensors work. Because IR light is everywhere (just like regular visible light) the IR sensor can't just look for IR light – it would read 'yup' all the time. Instead, it looks for IR light that is flickering at a particular frequency – which natural IR light does not do.
Our IR sensor is sensitive to IR light flickering at 38KHz, which means it's going on-off 38,000 times per second. Hard for us to turn a light off an on that quickly, but it's easy for our little microcontroller.
Have a look at:
examples/4-2-bounce_ir

All that we're adding is:
#include “recvNEC.h”
enableIROut();
Load it onto your badge with:
make install PROJECTNAME=examples/4-2-bounce_ir
Now wave your hand in front of the badge – does the red LED flash? If it does, you're bouncing an IR signal off your hand and onto the sensor! Blimey!
Now try to port this code into your colour cycling code, so that a bounced IR signal will reset the pattern.
(Hint – it should just be as easy as adding the two lines above!)
### Advanced Stuff
How come enableIROut() manages to send a valid 38KHz IR signal? Turns out that there's some magic buried in this function.
Look at:
includes/sendNEC.c
and find the enableIROut() function:
// turn on clock, prescale = 1
TCCR1 = _BV(CS10);
// toggle OC1B on compare match; PWM mode on OCR1C/B.
GTCCR = _BV(PWM1B) | _BV(COM1B0);

// these two values give 38khz PWM
// on IR LED, with 33%ish duty cycle
OCR1C = 210;
OCR1B = 70;

This is some of the fun stuff of using microprocessors – there are often hardware features that do some of the more awkward things for you – in this case setting up an extremely reliable 38KHz frequency on the 'OC1B' pin on the chip – which if you look at our chip pin out maps to PB4, where our IR LED sits.
How the hell does this work though?! It's just gibberish!
What is essentially happening is something that looks a little bit like this (thanks to Ken Sherriff, for making this even vaguely understandable – see http://www.arcfn.com/2009/07/secrets-of-arduino-pwm.html):

A Timer (which is essentially a counter from 0 to 255 (for an 8-bit timer) increments on each clock tick. Because this happens without fail, it's a very good reliable source of time – CPU ticks happen at a set frequency (8MHz in our case).
Here's where we need to start to look at datasheets. This will hurt a bit.
Let's look at it line by line:
// turn on clock, prescale = 1
TCCR1 = _BV(CS10);
This is just setting a bit in register TCCR1 ('the CS20 bit'). _BV is a macro that sets a specific bit in a byte.
Turn to p92 of the datasheet, and we can see what TCCR1 does: it controls Timer1 (the ATtiny has two timers).
Setting CS10 (bit 0) means that we're running at normal clock speed – so our timer will be incrementing at 8,000,000 (8MHz) ticks per second.
Dividing 8MHz by 256 means the timer gets reset to 0, 31250 times per second – good enough for us to do the quicker 38KHz.
// toggle OC1B on compare match; PWM mode on OCR1C/B.
GTCCR = _BV(PWM1B) | _BV(COM1B0);

P93 details GTCCR – and our bit setting of PWM1B here states “When set (one) this bit enables PWM mode based on comparator OCR1B in Timer/Counter1 and the counter value is reset to $00 in the CPU clock cycle after a compare match with OCR1C register value.”
So what happens here is 1) rather than reset the counter to 0 after it hits 255, we reset it when it hits the value of OCR1C – which from below we're choosing 210: 8.000,000/38,000 = 210 (ish). This gives us our PWM frequency.
The setting of OCR1B means that our pin will be HIGH until the clock reads '70', then will be toggled LOW. This gives us our 33% duty cycle.
// these two values give 38khz PWM
// on IR LED, with 33%ish duty cycle
OCR1C = 210;
OCR1B = 70;

Still with us? Head hurt?
We'll be doing a follow up course in the near future on how to read datasheets. They are not as hard as it first appears once you get used to some basic terms and layouts.